## Slide 1
Mechanics of an ICS/SCADA Man-In-The-Middle Attack

## Slide 2: Jim Gilsinn
Senior Investigator, Kenexis Consulting
  ICS Network & Security Assessments & Designs
  Developer, Dulcet Analytics, Reliability Monitoring Tool
Previous Life – NIST Engineering Lab
  20+ Years Engineering
  ICS Cyber Security & Network Performance
  Control Systems, Automated Vehicles, Wireless Sensors & Systems
International Society of Automation (ISA)
  ISA99 Committee, Co-Chair (ISA/IEC 62443 Standard Series)
  ISA99-WG2, Co-Chair (ICS Security Program)

## Slide 3: MITM Attacks Are Nothing New
Man-in-the-middle attacks have been around for a long time
They utilize loopholes in some of the basic network protocols
Allows an attacker to impersonate another device
There are TONS of videos and tutorials on the Internet on how to conduct a MITM attack
This IS NOT a talk about how to run a MITM attack

## Slide 4: What is this Talk About, Then?
This IS a talk about what happens to the systems when you run a MITM attack
ICS/SCADA rely on deterministic communications
How does a MITM attack affect those deterministic communications?
Can you detect a MITM attack using simple tools?
  Or, do you really need a full IDS system to detect it?

## Slide 5: Man-In-The-Middle Testing
Kali Linux VM
  Ettercap
  ARP Poisoning
  All default settings (script-kiddy style)
Captured traffic off mirror port
  Separate Kali Linux native machine with Wireshark
PLC to I/O
  EtherNet/IP™
  10ms frequency
MITM against PLC

## Slide 6: A Little Bit About EtherNet/IP™
Originally developed by Rockwell Automation
Now managed by ODVA, Inc.
Generally used at lower-levels in ICS/SCADA architecture
  Controllers (PLCs), HMI, I/O, motors, sensors, etc.
Level 4-7+ layer protocol
  Uses standard, unmodified TCP/UDP/IP stack
Has both command/response and publish/subscribe type communications
Command/response
  TCP – 44818
  Unconnected messaging
    No long-duration TCP connection
    Usually for initializing other connections
  Connected messaging
    Long-duration TCP connection maintained
    Periodic data transfers
Publish/subscribe
  UDP – 2222
  Real-time messaging
  Unicast from subscriber, multicast or unicast from publisher
  Allows multiple subscribers

## Slide 7: Description of MITM Attack – Hosts List
PLC
I/O Block
Netgear GS108E
MITM Machine
  Kali Linux 2.0 VM
  Ettercap 0.8.2 (default Kali version)
Capture Machine
  Kali Linux 2.0 Native
  Wireshark 1.12.?

## Slide 8: Description of MITM Attack – Targets
Target 1
  Main target of MITM attack
  PLC
Target 2
  Other target of MITM attack
  I/O Block

## Slide 9: Description of MITM Attack – ARP Poison
ARP Poison using “Sniff remote connections” option
Since network extremely small, other attacks didn’t work
ARP Poisoning seemed to get through relatively undetected
  VirusTotal
  NetworkMiner
  Bro

## Slide 10: Description of MITM Attack – Filtering
Filtered MITM Attack to modify EtherNet/IP-specific packet fields
Advanced sequence number by 5
Modified data value by adding 4 (decimal)

## Slide 11: Description of MITM Attack – Tests Conducted
Multicast I/O Block Publisher
  Baseline
  Baseline w/ button pushes
  MITM attack
  MITM attack w/ button pushes
  MITM attack w/ filter
  MITM attack w/ filter & button pushes
Unicast I/O Block Publisher
  Baseline
  Baseline w/ button pushes
  MITM attack
  MITM attack w/ button pushes
  MITM attack w/ filter
  MITM attack w/ filter & button pushes

## Slide 12: Connection Details
PLC
  MAC Address = 60:52:d0:05:58:70
  IP Address = 192.168.210.200
I/O Block
  MAC Address = 00:30:de:08:f8:7c
  IP Address = 192.168.210.5
PLC -> I/O Block
  10ms cyclic frequency
  Unicast
I/O Block -> PLC
  10ms cyclic frequency
  Multicast connection uses 239.192.1.128
VMWare
  MAC Address = 00:0c:29:87:b6:45

## Slide 13: Baseline

## Slide 14: Baseline
PLC -> I/O Block
~10ms cyclic frequency
~500µs distribution
I/O Block -> PLC
~10ms cyclic frequency
~400µs distribution

## Slide 15: MITM Attack – Multicast

## Slide 16: MITM – Multicast

## Slide 17: MITM – Multicast
I/O Block -> PLC
~10ms cyclic frequency
~400µs distribution
No Difference
PLC -> MITM
~10ms cyclic frequency
~400µs distribution
No Difference

## Slide 18: MITM – Multicast – IP-based analysis
192.168.210.200 -> 192.168.210.5
MITM instantly recognizable
Distribution extremely wide
Mean shifts down along distribution

## Slide 19: MITM – Multicast – MAC-based analysis – I/O Block Dst
Using the MAC address of the I/O block, isolate the traffic stream
MITM recognizable
Distribution recognizable
Mean remains the same

## Slide 20: MITM Attack – Unicast

## Slide 21: MITM – Unicast

## Slide 22: MITM – Unicast
I/O Block -> PLC
~10ms cyclic frequency
~400µs distribution
No Difference
PLC -> MITM
~10ms cyclic frequency
~400µs distribution
No Difference

## Slide 23: MITM – Unicast – IP-based analysis
192.168.210.5 -> 192.168.210.200
MITM instantly recognizable
Distribution extremely wide
Mean shifts down along distribution
Herringbone pattern probably due to clock skew

## Slide 24: MITM – Unicast – MAC-based analysis – PLC Dst
Using the MAC address of the PLC, isolate the traffic stream
MITM recognizable
Distribution recognizable
Mean remains the same

## Slide 25: MITM – Filter
Additional testing was conducted to see if filters caused any performance differences
The intent wasn’t to do an awesome Stuxnet-type attack
Adjusted sequence number to spoof out the signals
Modify the I/O data in the packets to change light action related to button pushes

## Slide 26: MITM – Filter – Base Button Pushes
Buttons | PLC->I/O Unfiltered | I/O->PLC Unfiltered | PLC->I/O Filtered | I/O->PLC Filtered
0 0 0 0 | 0x00 | 0x55 | 0x04 | 0x55
1 0 0 0 | 0x01 | 0x56 | 0x05 | 0x56
0 1 0 0 | 0x04 | 0x59 | 0x08 | 0x59
0 0 1 0 | 0x10 | 0x61 | 0x14 | 0x61
0 0 0 1 | 0x40 | 0x95 | 0x44 | 0x95

## Slide 27: MITM – Filter

## Slide 28: Captures
I hope to post the capture files shortly
Check my Twitter feed for more info
I need to get approval first
EDIT:
Capture files available at

## Slide 29: Questions & Comments?
Jim Gilsinn
Senior Investigator, Kenexis
+1-614-323-2254
Jim.Gilsinn@Kenexis.com
@JimGilsinn